## Slide 1: Wave-front sensing / control
R&D activities for Space applications
2017 ITHD-II Workshop

## Slide 2: Wave-front control (PhD Lucie Leboulleux)
Collaboration STScI
Error budget for studying space high contrast sensitivity to aberrations on segmented pupils
  Simplified analytic model for wide exploration
  End-to-End model (COFFEE library) for precise coronagraph modelisation.
Non linear Dark Hole
  Non-linear => 1 shot application
  Model-based technique
    DM, Pupil shapes, Amplitudes effects, Coronagraph (focal + apo)
  Perspectives
    Application on HiCat
    Application on THD (CNES, link to O. Herscovoci PhD)
Science Camera
WFS (Coffee)

Non-linear DH
 (voltages)
AO sytem (DM)
Coronagraph
Light source
O. Herscovici
L. Leboulleux
Validation on MITHIC

## Slide 3
TWO DEFORMABLE MIRRORS : continuous and segmented
JWST pupil, Rodier-Rodier coronagraph,

## Slide 4: Multi-DM achromatic correction
Problem: Chromatic aberration of the instrument limits the efficiency of coronagraphic instruments (Broadband Spectroscopy)
Purpose: To use multiple DMs to correct residual chromatic aberrations
Current activities (LESIA):
  Theoretical, algorithm aspects and experimental tests on THD2 (collab Netherlands, SRON)
  Dvlpt of efficient components over wide band for testing on THD2

## Slide 5: Multi-DM amplitude correction
Problem: Amplitude aberrations of the instrument limits the efficiency of coronagraphic instruments
Purpose: To use multiple DMs to correct amplitude aberrations
Current activities (LESIA):
  Theoretical and algorithm aspects (collab with Nice Obs.)
  Experimental tests on THD2
FDH correction below 3 10-8 between 5 l/D and 10 l/D
(Baudoz et al. in prep)

## Slide 6: 1ère démonstration expérimentale de “COFFEE complexe”, sur le banc THD
PhD Olivier Herscovici
Recherche aberrations de phase et d'amplitude pour très haut contraste
Collaboration LESIA, financement R&T CNES
Résultats :
  Étalonnage fin de ce qu’introduit vraiment le DM Boston
  Mesure d’aberration d’amplitude sinus, 11 cycles/pupille à 45°:
  Perspectives :
    dépouillement nouvelle campagne de mesure (vs SCC)
    correction par dark-hole non linéaire : à venir (R&T en cours)
Avec défaut d’amplitude / sans défaut / différence ;) !

## Slide 7
Self-CoherentCamera (SCC) & Multi Reference SCC (MRSCC)
Spatial encoding of the speckles in focal plane :
Estimation of the complex field
Not model dependent
One (MR)SCC image (= science image) per correction loop
Proven Closed-loop correction (at ≈10 Hz) in the lab at 108 contrast with bandwidths (1 to 80 nm in the visible)
SCC = 1 reference pupil
MRSCC = 2 to 3 references