## Slide 1: SPHERE – SAXO Performance status

## Slide 2: Performance de SAXO : biblio
SPIE 2014
AO4ELT 2015
SPIE 2016
JATIS 2016

## Slide 3: SPHERE Internal performance
NCPA status on SPHERE
  Residual WFE better than specification (42nm) without HO-NCPA compensation
  Only centering / focus optimised on corono (before each observation)
  Phase conjugation could improve, but dead actuators makes the process complex
Future improvements
  Use of Zelda NCPA measurements
  Focal plane estimation with coronograph in place (COFFEE / EFC)
Residual NCPA | 42nm RMS
Strehl Ratio in H | 97%
UPDATE OF THIS PERF ?
Long-term variations ?
Actions to get it regularly ?
ZELDA-NCPA confirmation of ~40nm RMS ?

## Slide 4: Spatially filtered SH
Spatial filter: nominal performance
Operation: Optimisation of SF with respect to turbulence strength
Conservative choice for robustness reasons,
Expert parameter allowing improved performances at low seeings
Gain x 3
Statistic of Spatial Filter sizes ?
Optimisation ?
Engineering mode used or not ?

## Slide 5
Theoretical performance reached
Limit magnitude 14/15
Max perf 91% SR in H
Max perf up to mag 9.5
Perf vs magnitude Commissionning data

## Slide 6: SAXO turbulence/performance estimator
SPARTA provides estimation of turbulence every minut (r0, wind, SR)
Measurement compared to different sources during COMs
Truth sensor = Seeing in Open-Loop images
SPARTA estimation validated
Discrepancy wrt DIMM (as already noticed on other instruments)
Atmosphere monitoring : best estimation by AO system itself

## Slide 7: SAXO telemetry data
r0
DTTS Flux
SR
SR
DTTS images

## Slide 8: SPHERE main limitation: From AO residual to Quasi-static speckle
GQLupi
HIP 43620
HIP 73 145
Tcha
Wind speed
Limited by AO residual
Limited by QS residuals

## Slide 9: Perf vs magnitude from commissioning to operation
Disentangle system calibration issues from external environment perturbations

## Slide 10: Further understanding: ZELDA measurements
ZELDA : WFS based on Zernike phase mask (M. N’Diaye 2013 a&a),
  pupil plane observable, high spatial resolution
Sharp & strong phase discontinuities around spiders
Up to hundreds nm phase step
Piston, Tip and Tilt on each segment
Typical discontinuity size ~ Spider width => Smaller than the pitch

## Slide 11: Physical origin of the problem: heat exchange
Scenario today: temperature difference around the spider
The lower the wind speed, the more efficient the heat transfer between spider and air
1 degree difference, 1m height is enough to create 800nm OPD
Temperature measurement at Paranal, UT3
Tair
T ’air
Tspider<Tair

## Slide 12: Air flow simulation (M. Brinkmann, ESO)
Numerical CFD simulations ANSYS
Simplified 2D geometry => quick exploration of parameter space
Tests with different flushing velocities / heat level
Initial values for Tspider from rough estimation, to be refined by FEM simulations
Scenario confirmed !
Work in progress (heat values, 3D models, temperature probes…)
Use ANSYS simulation outputs to produce LWE profile
Velocity 3.0m/s
Velocity 0.9m/s
Velocity 0.3m/s

## Slide 13: SPHERE Low Wind Effect – ongoing actions
Focal-plane WFS methods
  Phase diversity (JF Sauvage)
  Pupil diversity (F. Martinache)
  Bench validations (MLamb, MWilby)
Compensation as a NCPA
  Validation on SPHERE
Change of the coating of spiders on VLT UT3